## Slide 1: Math Library Overview 2023 DARTS Lab Course
Abhinandan Jain, Aaron Gaut, Carl Leake, Vivian Steyert, Tristan Hasseler, Asher Elmland, Juan Garcia Bonilla

## Slide 2: Outline
Linear algebra
  Vectors (SOAVector, SOAVector3)
  Matrices (SOAMatrix, SOAMatrix33, …)
Attitude representations
  SOAQuaternion, SOARodriguezVector, SOAEuler, …
Homogeneous transforms
  SOAHomTran
Spatial notation and rigid body quantities
  Spatial vectors (SOASpatialVector)
  Spatial inertias (SOASpatialInertia)

## Slide 3: Documentation & Resources
SOA Doxygen docs
SOA Sphinx documentation
SOA doctests
The key math classes live in the SOA module, and the class names have the ‘SOA’ prefix
SOAVector
SOAMatrix
SOAQuaternion
…
Course 2020 slides and videos

## Slide 4: Vector Classes

## Slide 5: SOAVector (Notebook: B-Preliminaries/01-SOAVector)
The SOAVector class for vectors
variable length, fixed length
creating from Python lists
the dump, pydump and call method

## Slide 6: SOAVector3 (Notebook: B-Preliminaries/02-SOAVector3)
The SOAVector3 class for 3-vectors
includes methods such as tilde, cross, etc.

## Slide 7: Matrix Classes

## Slide 8: Matrix classes
Similar to SOAVector/SOAVector3 we have the SOAMatrix, SOAMatrix33, SOAMatrix66 classes for matrices
Overloaded operators
Getting/setting values, the call() method
The dump and pydump methods
Various matrix methods

## Slide 9: SOAMatrix (Notebook: B-Preliminaries/03-SOAMatrix)
variable size
creating from Python lists
the dump, pydump and call methods
various operations

## Slide 10: Attitude Representations

## Slide 11: Attitude Representations
The attitude of frame B with respect to frame A can be defined as a rotation about a fixed axis
(exponential formula)
(angle/axis)
(unit quaternion)

## Slide 12: Accumulation of Rotations
Can compute rotations by composing successive ones.
indices must match when composing

## Slide 13: Available attitude representations
Representations & classes
  Rotation matrices (SOARotationMatrix) [9 scalars]
  Unit quaternions (SOAQuaternion) [4 scalars]
  Euler angles (SOAEuler) [3 scalars]
  Rodrigues parameters (SOARodrigues) [3 scalars]
  Angle/axis parameters [4 scalars]
General result: minimal (3 scalar) attitude representations cannot both be global and non-singular.
  See QA entry 597 for more details
  Euler angle & Rodrigues params are global, but singular
  Cayley representations are non-singular, but not global
minimal

## Slide 14: SOAQuaternion (Notebook: B-Preliminaries/04-SOAQuaternion)
An overview of the SOAQuaternion class

## Slide 15: Attitude Representations notebook (Notebook: B-Preliminaries/05-attitude_representations)
Euler angles
Rodrigues parameters
Rotation matrices

## Slide 16: Homogeneous Transforms

## Slide 17: Working with both position/rotations
Typically have to deal with both rotations and displacements simultaneously.

## Slide 18: Homogeneous Transform
Combined attitude and position information is also referred to as “pose”.
A pose can be represented as a 4x4 homogeneous transform matrix.
SOAHomTran
class
Inverse:

## Slide 19: Propagating pose across frames
Computing overall relative pose by composing component poses (like rotations)
relative position
Propagates positions and rotations simultaneously
composing homog. transforms

## Slide 20: Propagating Poses
Frequent need to compute poses of bodies and frames with respect to each other and the inertial frame.
constant
constant
variable

## Slide 21: Composing Homog. Transforms
Claim:
Verification:

## Slide 22: SOAHomTran (Notebook: B-Preliminaries/06-SOAHomTran)
Products
Getting translation/quaternion elements
Transforming a position

## Slide 23: Rigid Bodies & Spatial Notation

## Slide 24: Linear/Angular properties
When working with kinematics and dynamics, we often have to work with a combination of linear and angular properties
  position/attitude
  linear/angular velocities
  force/moments
  linear/angular momentum
  mass/inertia
Only at the body CM are the position & angular properties mostly decoupled
However, general, non-CM reference frames are often used – leads to messy coupling
CM
ref
frame

## Slide 25: Spatial Notation
"spatial" notation – combines linear & angular terms together to help work with general (and not just CM) frames
  position/attitude: homogeneous transform
  velocities: spatial velocity [w, v] 6-dimensional
  accelerations: like-wise
  forces: spatial force [N, F] 6-dimensional
spatial velocity
spatial force
SOASpatialVector
class
See Spatial Operator Algebra book reference for details
moment
force

## Slide 26: Transforming spatial velocities across a rigid body
Consistent way to transform spatial velocities across any pair of points on a rigid body
SOAHomTran.PHIStar method
QA entry 31
Uses components of the T(A,B) homogeneous transform

## Slide 27: General spatial velocity transformations
Can accumulate spatial velocities across multiple frames
Example: A is inertial frame, and want inertial spatial velocity of C given inertial velocity of B, and C wrt B (eg. hinged bodies)
Inertial frame
hinge
QA entry 31

## Slide 28: SOASpatialVector (Notebook: B-Preliminaries/07-SOASpatialVector)
Overview of the spatial vectors class

## Slide 29: Transforming spatial forces
Can transform forces and moments across points on a rigid body
SOAHomTran.PHI
method
QA entry 31
forces
moments

## Slide 30: Accumulating Spatial Forces
There is often a need to compute the overall spatial force on a rigid body, eg. from attached actuators
The process is to transform each of the forces to a common point, and then sum them up as follows
overall spatial
force at B
transform spatial
force to B

## Slide 31: SOAHomTran Phi/PhiStar (Notebook: B-Preliminaries/08-RigidBodyTransformations)
Transforming spatial velocities
Transforming spatial forces
The PHI and PHI_star methods

## Slide 32: Spatial Inertias

## Slide 33: Rigid body inertias
Mass properties of a rigid body are characterized by
  Scalar mass, m
  First moment of inertia 3-vector p (vector from the body frame to the CM)
  Second moment of inertial, 3x3 inertia matrix J
Traditionally these terms are kept apart in the linear and angular equations of motion
  This works well only at CM
  Otherwise get nasty cross-coupling terms

## Slide 34: Rigid body spatial inertia
Spatial inertia of a rigid body about CM
Spatial inertia of a rigid body about any point
SOASpatialInertia class for spatial inertias

## Slide 35: Transforming Spatial Inertias
General way to transform spatial inertias across any pair of points on a rigid body
Parallel axis theorem
SOASpatialInertia.parallelAxis() method
Simpler, and more compact than conventional parallel axis theorem for 3x3 rigid body inertias.

## Slide 36: Combining spatial inertias
Often need total effective mass properties of a collection of bodies
Requires transforming all mass properties to a common point (parallel axis theorem) and then adding them together

## Slide 37: SOASpatialInertia (Notebook: B-Preliminaries/09-SOASpatialInertia)
Constructing them
Getting the matrix form
Parallel axis theorem

## Slide 38: Rigid Body Kinetic Energy
Body kinetic energy can be defined by the spatial inertia and spatial velocities
Kinetic energy is invariant to reference point when working with spatial quantities. Indeed
This is a generalization of the well know quadratic expression for positional and angular energies at the CM

## Slide 39: Spatial Transformations Recap
Spatial notation offers concise & consistent transformation expressions for arbitrary non-CM points
Spatial velocities
Spatial inertia
Spatial forces
Kinetic energy
Spatial momentum

## Slide 40: Recap
What are the matrix/vector library classes?
  SOAVector, SOAMatrix classes
How are the C++/Python software languages being used?
  C++ for all heavy lifting with SWIG generated Python bindings for usability
What are the supported attitude representations?
  Mainly unit quaternions, but also rotation matrices, Euler angles, Rodrigues parameters, angle/axis representations
What are the aerospace & robotics conventions for rotations?
  Geared to transform ‘from’ vectors to ‘to’ vectors – or the other way around
How do we use unit quaternions?
  Via the SOAQuaternion class for all attitude representations
How do we use homogeneous transforms?
  Via the SOAHomTran class for all pose representations
What are spatial velocities, forces, inertias and momentum?
  Combined linear and rotational 6-d quantities
Why use spatial notation in kinematics and dynamics?
  Makes rigid body transformations much simpler & concise via Phi and PhiStar methods

## Slide 41: What we did not cover …
Attitude representations – rotation matrix, Rodrigues parameters
Various matrix methods
Interpolation classes
Lie group connections
  Different types of spatial velocity definitions
  PhiStar/ad connection
More phi/phistar properties
Quadrature integration
Coriolis terms for acceleration accumulation (methods exist) - see QA site