## Slide 1: Frames Layer 2023 DARTS Lab Course
Abhinandan Jain, Aaron Gaut, Carl Leake, Vivian Steyert, Tristan Hasseler, Asher Elmland, Juan Garcia Bonilla

## Slide 2: Simulation tree of frames
Examples of frames:
  location of a thruster on the s/c bus
  the motion of a pair of frames due to hinge articulation
  the motion of the moon wrt to the earth; the earth wrt the sun etc.
Frames form a tree with edges defining transform between adjacent ones
DFrame Sphinx docs
DFrame Doxygen docs
Course 2020 slides & video

## Slide 3: Motivation
Simulations can have many moving frames, e.g.
  Bodies, nodes, planetary bodies, CM frame …
Often, ask what is the pose (position/velocity etc.) of a frame?
  These are INCOMPLETE questions! There is an unspecified but implied “from” frame (often inertial frame)
Steps involve sequences of Phi/PhiStar etc transformations across path in the tree
  Error prone, time consuming and tedious
The DFrame frames layer provides a simple way to make such queries for arbitrary pair of frames

## Slide 4: Frame & Frame2Frame software classes

## Slide 5: Working with DFrame frames
DFrame module provides the Frame and Frame2Frame classes
The FrameContainer class is a container class for all frames
Some frames come for free
  Bodies, nodes, planetary bodies are automatically Frame instances
  Frames for CM locations are automatically created
However, users can create, add, or reattach arbitrary frames
  Users/simulation is only responsible for updating the transform etc. properties of each parent/child frame pair edge
  For rigid attachments, this is a one time step

## Slide 6: Frames (Notebook: B-Preliminaries/10-Frames)
Creating
Attaching
Showing in 3D graphics

## Slide 7: Frame’s are base classes for Bodies & Nodes
Location of interest
Location on a body
Has extent and mass properties
Can apply forces
For an inter-body hinge
Articulated body related classes

## Slide 8: Frame to Frame relationships
Frame2Frame objects define relationships between oframe/pframe pairs.
They can be used to obtain relative transforms, velocities accelerations
Joint angles and rates modify edge properties

## Slide 9: Frame2Frame Class
Consists of a frame pair – <oframe, pframe>
Used for quantities relating one frame to the other
  Homogeneous transformation
  Relative velocity
  Relative acceleration
Can compute relative velocity and acceleration with derivatives taken wrt another frame
  Requires <derivFrame, oframe> Frame2Frame
  Default derivatives are wrt oframe
Same for acceleration

## Slide 10: Arbitrary pair of frames
ChainedFrame2Frame class manages arbitrary oframe/pframe pairs in the tree.

## Slide 11: ChainedFrame2Frame
ChainedFrame2Frame instance are objects that have a beginning (oframe) and an end (pframe)
have all the smarts to chain together all the computations needed to compute the relative properties
know the connecting path
can do reversals across branches as needed
can handle changes to paths
only compute on demand
cache results, and recompute only if any of the edges has changed!

## Slide 12: Recipe for frame to frame use
Create a frame container instance and populate it with frames, and form edges to connect them
Identify the oframe/pframe frame pair you are interested in
Use oframe.frame2Frame(pframe) method to get the Frame2Frame instance (edge or chained)
Use the frame to frame instance methods to get information
  relTransform(): returns the relative pose
  oframeDerivRelSpVel(): returns the relative spatial velocity as observed from the oframe
  oframeDerivRelSpAccel(): returns the relative spatial acceleration as observed from the oframe

## Slide 13: Frame2Frame (Notebook: B-Preliminaries/11-Frame2Frame)
Creating a Frame2Frame
Making relTransform, vels, accels queries
Dumping

## Slide 14: Computational Aspects
For N frames, have potentially N(N-1) frame to frame pairs
  Too expensive to keep all combinations up to date
On demand computation
  Do not compute and update properties of all existing frame 2 frame pairs with every motion – only on demand
Cache frame to frame property values until a component edge value changes to make path value stale
  Only recompute stale values

## Slide 15: Frame2Frame’s are base classes for body hinges
Family of frame to frame classes
Frame2Frame
EdgeFrame2Frame
Parent/child frame pair
PrescribedFrame2Frame
Frame pair with user specified relative transforms
DartsSubHinge
Darts body hinge
DartsHinge
Darts body subhinge
Abstract base class
ChainedFrame2Frame
Sequence of connected Frame2Frames
Bodies specialization

## Slide 16: Spice Frames

## Slide 17: Spice Frames
The SpiceFrame class is a Frame class with a NAIF id
The SpiceFrame2Frame class is a EdgeFrame2Frame class where the oframe & pframe pair are both SpiceFrame instances
  Can use the Spice library to query the location of celestial bodies (and spacecraft)

## Slide 18: SpiceFrame (Notebook: B-Preliminaries/12-SpiceFrames)
Creating SpiceFrames
Querying planetary transforms
Changing times to change values

## Slide 19: Frames Layer
The frames layer provides a unifying foundation for most of the simulation related objects, allowing pose etc queries to be easily made across diverse domains.
Celestial
bodies
Multibody
world
Control
frames
Visualization
frames
Frames Layer

## Slide 20: Recap
What are frames?
  Any point of interest, eg. bodies, attachment points, terrains, celestial bodies, center of mass location and instances of the Frame class.
What are frame to frames?
  These are Frame2Frame instances for a oframe/pframe pair that can provide relative pose, velocity etc. information
How can we get position/attitude, velocities of arbitrary frames?
  By using the from.frame2Frame(to) chained frame to frame
What does the frame layer buy you?
  Does away with custom user code for querying relative pose information.
How are the computational costs low despite the flexibility?
  By use of lazy evaluation and data caching.
What are key classes derived from the frame classes?
  Bodies, nodes, subhinges and hinges are derived from these classes.
What are SpiceFrames?
  Frames with NAIF ids whose pose is obtained via the Spice library.
What is the a way to visualize frames?
  By using the viz show() and showFrame2Frame() methods.

## Slide 21: What we glossed over/skipped …
More exotic methods
  other derivatives
  Coriolis terms
Can attach/detach frames
Fixed, prescribed, and unrotated frames
looking up frames
dumping frames tree
Defining custom update callbacks for transforms, velocities, etc.