## Slide 1: Dshell Models
Abhinandan Jain, Aaron Gaut, Carl Leake, Vivian Steyert, Tristan Hasseler, Asher Elmland, Juan Garcia Bonilla

## Slide 2: Where does this topic fit in …
Dynamics
Rigid/flex bodies
Articulation
Attach/detach etc
Devices
Thrusters, IMU,
Cameras etc
Environment
Terrain, Gravity
Atmosphere,
Ephemerides etc
Geometry
CAD parts
Primitives
Visualization
3D graphics
stripcharts
Analysis
Data logging
Parametric
Monte Carlo
Closed-Loop
Flight s/w
Autonomy/Control
Usability
Introspection
CLI, GUIs, Scripting
Docs, Training
Knowledge base
S/W Mgmt
Version control
Build system
Test suite
Reusability
Architecture
Configurability
Refactoring
Deployment
Bundling
Porting
Issue tracking
Evolution
R&D, new applications
new tools & capabilities
Sim Manager
propagation, fsm,
events

## Slide 3: Assemblies create the simulation backbone: multibody, models, and data flow
Emergent multibody model
Assembly hierarchy
Asm1
Asm2
Asm3
Asm4
Asm5
mdl1
mdl2
mdl3
mdl4
mdl5
bd1
bd2
bd3
Emergent model dataflow
Run-time
Construction
An Assembly is a Factory creating dataflow and multibody models
The purpose of an Assembly is to construct the multibody, models, and data flow.
Once that is complete, the assembly’s work is done and is not generally needed at runtime
Python
C++

## Slide 4: Dshell Models – Background
Our goal is to model physical systems
  Spacecraft, ground vehicles, robots
Physical systems are composed of low-level devices or subsystems such as encoders, IMUs, thrusters, etc and interactions with the environment
We will use Dshell Models to simulate or “model” these components
  These models are DARTS aware, and can hence get and set data with the vehicle dynamics layer
  The component models can be assembled into a data flow and exchange data with other models as well

## Slide 5: Goals of Dshell Models
Model a wide range of devices and subsystems
  Devices that interact with the multibody system
  Other devices/subsystems not directly related to the multibody (eg, batteries)
Fast simulations (implemented in C++)
Reusable
  Support multiple instances in one simulation (perhaps with varying parameters)
  Reusable across different simulations
  Scalable in performance & fidelity
  Clear limited interface allows drop-in replacements to improve fidelity or reduce fidelity (faster)
  Enforce encapsulation (Information hiding to reduce coupling)
Analogous to Simulink S-functions, except that Dshell models have DARTS interfaces for getting and setting dynamics data crucial for vehicle dynamics simulations

## Slide 6: Parallels with Simulink
Similar components based approach
  Both use component models and dataflows
Key difference is the presence of the DARTS multibody dynamics block in Dshell for our vehicle dynamics focus
  Dynamics models are complex and is computationally expensive
  Dynamics has interfaces to most of the models (many signal lines in and out)
  Interfaces depends on the specific mechanism and other models in the sim
  We treat DARTS as a foundational middleware available to all the components
  Matlab/Simulink is more general purpose
Image by By Thomas Haslwanter [CC BY-SA 3.0], via Wikimedia Commons

## Slide 7: Dshell Model Classes
DartsModel
  ContinuousModel: supports continuous states independent of the multibody
  NodeModel: Act/Sense body nodes:
    Actuator / Sensor
  HingeModel: Act/Sense hinges:
    Motor / Encoder
FlowModel
  Independent of multibody, no continuous states (eg, GNC)
Models are a C++ classes which models devices, components, or environment entities
  Implements governing equations/logic
  Self-contained

## Slide 8: Available Dshell Models?
Module (selected) | Types | Continuous | Actuators | Sensors | Motors | Encoders | Flow
AeroModels | Aerodynamics |  | 1 | 5 |  |  | 1
AeroPythonModels | Aerodynamics |  | 1 |  |  |  | 
CameraImageModels | Camera imaging |  |  | 6 |  |  | 4
GeneralModels | Misc, mostly basic | 2 | 14 | 16 | 28 | 5 | 4
GravityModels | Gravity |  | 15 |  |  |  | 
AdvancedGravityModels | Gravity |  | 4 |  |  |  | 
DshellCommonModels | Misc |  | 3 | 7 | 1 | 2 | 
PowerModels | Power |  |  |  |  |  | 4
RoboSimianModels | Robotics |  |  |  | 6 |  | 
RoverDynModels | Rovers mechanisms |  | 4 | 7 | 11 | 3 | 3
RoverHdwModels | Rovers sensors |  |  | 3 |  |  | 15
RoverNavModels | Rover navigation |  | 5 | 2 |  |  | 23
RoverppModels | Rover |  |  |  |  |  | 3
SurfaceContactModels | Vehicle-soil interaction |  | 20 | 4 |  |  | 
VehicleModels | Spacecraft models |  | 14 |  |  |  | 
 | Total | 2 | 81 | 50 | 46 | 10 | 57
(All 70 modules: > 500 models)
Total in these modules: 246

## Slide 9: Dshell Model Basics

## Slide 10: Dshell Model example
Example – Rotor Thrust Model
Rotor Thrust Model (“Actuator”)
W = Rotor Speed
Compute Thrust
F = k*W*W
Parameter k
Rotor Speed
F
Apply force F to a body

## Slide 11: Dshell Models
Models emulate component behavior
  Contain model states and perform computations to model the device or subsystem
  Take data in (“flow inputs”) and put data out (“flow outputs”)
  Model interconnection into data flow via signals
  Customized via parameters
  Interact with multibody (optional)
Reusable C++ component models with ability to sub-class
Auto-code generator - with support for template revisions using Python
Dshell Model Sphinx documentation
Model 2
Signal A
Model 1
DARTS Multibody/Flexbody Engine
Flow Outputs
Flow Inputs
Parameters
Actuator and Sensor Models access Vehicle Data from attachment Node
State Variables
- discrete
- continuous
- scratch Variables
Commands
Fault Injection

## Slide 12: Dshell Model Internal Data
Parameters (‘params’)
  Used in modeling computations
Discrete states (‘states’)
  Track model state (changed by model logic)
Continuous states (‘cont_states’)
  Models set derivatives, system integrates
Scratch variables (‘scratch’)
  Intermediate calculations, data for debugging
flowIns/flowOuts (‘flow_in’ / ‘flow_out’)
  Provide/get data to/from other models
The data in these can be scalar or vectors of: floats, int, enums, bool, user-defined structs, pointers, and strings
F = k*W*W
 mode

## Slide 13: Dshell Signals for Connecting Models
Models are “black boxes” – with limited interaction between them except via connections (information hiding)
Connections between models are through “signals” – shared data buffers
Signals are data buffers for:
  Floats, integers, etc
  Vectors of floats, integers, etc
  Slices of vectors
    allow splitting signal vectors to multiple modes
Models have FlowIns & FlowOuts to connect to signals.
Models do not create signals!
Black box!

## Slide 14: Dshell Models – Data Flow
Note that upstream models must have their computations done before downstream models!
Model execution order must be determined in advanced (sorted) for the proper execution order
The way that models are connected creates a “data flow”
Model A
Model C
Model B
Model D

## Slide 15: Notebook: Creating Signals
Demonstrate creating signals of different data types
  Scalar and vector values signals
  Creating signal slices, and slices from slices
E-Dshell/Part-2-Models/01-Basic-use-of-signals

## Slide 16: Notebook: Signals & Models
Demonstrate using signals with a model
  Demos signal freshness and re-tying signals
E-Dshell/Part-2-Models/02-Use-of-signals-in-a-model

## Slide 17: Notebook: Using signal ties
Demonstrate using signal ties in a run script to connect signals and models at lower levels of the assembly hierarchy
E-Dshell/Part-2-Models/03-Tying-signals-in-run-scripts

## Slide 18: Dshell Models + Multibody
S
Multibody
System
…….
..... ...
Body i
Body j
Motor
F
F
F
F
S
Flow models
Body k
Body m
F
F
S
A
Connections / Hinges (Darts) Flow Connections (Dshell)
A Actuators Models M Motor Models
S Sensor Models E Encoder Model F Data Flow Models
…
Actuator
…
M
E
Sensor
Encoder

## Slide 19: Assemblies + Models + Multibody
Detailed examination of a Rocky 8 rover simulation model including the assemblies, multibody structure, the models and the signals
E-Dshell/Part-2-Models/04-Roams-models

## Slide 20: Defining a Model Class

## Slide 21: Basic Model Information
Model definition file (*.mdl) used for model interface definition and creation
  Defines the parameters, states, inputs and outputs for a model
  Available at runtime via model meta data function
Boiler plate C++ code is auto-generated from the mdl files
The parameter, states etc. data is can be accessed at run-time access through Dvar “specNodes”
Data is also used by other sim-related tools
  Dshell GUI simulation data browser
  model linker

## Slide 22: Model “mdl” interface definition
The model .mdl file example
This metadata can be accessed at runtime
[Type]
Name = PinEncoder2
Kind = encoder
Keywords = {Hinge!Pin}
[params]
[[polarity]]
Type = int
Length = -
Brief description =
"""Sign convention"""
[scratch]
[[gearRatio]]
Type = double
Length = -
Brief description = """gear ratio of hinge"""
Long description = """"""
[states]
[[offset]]
Type = double
Length = -
Brief description = """Joint angle offset"""

## Slide 23: Model & Signal Introspection
Introspect with DVar specnodes
  From command line
    model.specNode()
    signal.specNode()
  From Dshell gui

## Slide 24: Model Spec Node
Model data is accessible through its “spec Node” (the DVar interface)
Steps:
  Get the model object specnode
    >>> sp = model.specNode()
  Peek / Poke its data
    >>> sp()  get python dictionary of all model data
    >>> sp[‘param.R’]()  get value of parameter ‘R’
    >>> sp[‘param.R’](1.5)  set the value of R to 1.5

## Slide 25: Dshell gui
Much easer to use the Dshell GUI!
  sim.gui()

## Slide 26: Notebook: Model Instancing & Inspection
Demonstrate creating model in a run script and creating and tying signals to it
  E-Dshell/Part-2-Models/08-Create-model-in-script

## Slide 27: Notebook: Interacting with Models
Shows details of interacting with a basic dosimeter model
  E-Dshell/Part-2-Models/09-Basic-model-interactions

## Slide 28: Notebook: Accessing Model Metadata
All a model’s data defined in its ‘*.mdl’ file is available at runtime without a live instance of the model.
This notebook shows details of accessing model meta data at runtime
  E-Dshell/Part-2-Models/10-Accessing-model-metadata

## Slide 29: Data Flow Model Order

## Slide 30: Data Flow Model Execution Order
What order do models get executed in within the models data flow?
Model order must conform to the physics of the modeled system and logic of the simulation
Model (A) whose flowOuts go to some other models (B) flowIns implies that Model A must be executed first since it is "upstream“
  Some exceptions here that will be explained later
Most of model order determined from model flows (the rest is arbitrary but lexically ordered for repeatability)
Model sorting is automatic
Model sort loops can occur. To resolve we may need to add:
  Model break (ignore connection between two models during sort)
  Model constraints (force one model to be "upstream" of another)
Model A
Model C
Model B
Model D
First
Second
Third

## Slide 31: Example Model Ordering
Model A
Model C
Model B
Model D
After Sorting:
Arbitrary ordering resolved by alphabetical sorting
Precedence:
A → B
A → C → D
A, B, C, D
or
A, C, B, D
or
A, C, D, B
Equivalent

## Slide 32: Simulation Model Data Flows
Flow DebugFlowAdvanceDynamics
Encoder Dyn Model D1
Actuator Dyn Model D2
Motor Dyn Model D3
Flow Model F1
Flow Model F2
Sensor Dyn Model D4
Flow Model F3
Model Order: F1 → F2 → [ D2 → D5 → D1 → D3 → D4 ] -- > F3
Flow Models (no continuous states, advance with tick)
Dynamic models (continuous states or interacts with DARTS)
Continous Model D5
DARTS

## Slide 33: Flow Model Loop Notebook
Demonstrate breaking a flow models loop by adding a flow break for the purposes of flow model order sorting
  E-Dshell/Part-2-Models/05-Model-add-flow-break

## Slide 34: Dynamics Model Loop Notebook
Demonstrate breaking a dynamics models loop by adding a dynamic break for the purpose of dynamics model order sorting
  E-Dshell/Part-2-Models/06-Model-add-dynamic-break

## Slide 35: Inter-Model Constraint Notebook
Demonstrate forcing a specific order using a model order constraint when there are multiple potential orderings possible (due to partial ordering)
  E-Dshell/Part-2-Models/07-Model-add-order-constraint

## Slide 36: Standard Model Methods

## Slide 37: Dshell Model Methods
All Models
constructor Any model-specific setup
setup()
processParams() Install provided parameters into local data Any necessary auxiliary calculations
updateFlowOuts() Compute new values for flowOuts and update the flowOuts so signals get updated
Etc (eg, user defined)
Darts/Continuous Models
preDeriv() / postDeriv() – Functions that are called to interact with the multibody system
beginIOStep() / endIOStep() – functions that will
beginIntegration() / endIntegration()
Etc (eg, user defined)
Flow Models
hop() – advance the internal logic or governing equations

## Slide 38: More about Model Design
Models only interact with the DARTS multibody object through bodies, nodes, etc., directly assigned to them
  Can access their body/joint
  A model cannot “see” the rest multibody system!
Models with continuous states only interact with their own states, not the “big X” state vector
  Can see their continuous states
  Can only set derivatives for their continuous states
Such information hiding is a key design feature of models to use information hiding to reduce coupling across the models and simulation complexity

## Slide 39: Instancing a Dshell model

## Slide 40: Creating a model instance
Process:
  Chose Dshell model to instantiate
  Create/obtain signals to be connected to the model flowIns/flowOuts
  Tie signals to flowIns / flowOuts
  Set parameter data
Dshell Assemblies are typically used to manage models and signals creation and tying them to create the dataflow
  Assemblies usually create the multibody, models, and data flow
  Assemblies are not needed for state time propagation
  Note: An Assembly keeps track of the models that it creates
Flow Outputs
Flow Inputs
Parameters
Actuator and Sensor Models access Multibody Data from attachment Node
State Variables
- discrete
- continuous
- scratch Variables

## Slide 41: Example Model Instancing
After creating the model, it needs to have its model parameters set
asm.addSignal('signame', {'length': 1, 'type': 'double',
'comment': 'signal description)
mdl = asm.addModel('mdlname', 'encoder', {
'MODEL_TIES': encoder_ties,
'class': 'PinEncoder',
'comment': 'encoder model',
'outb': body})

## Slide 42: Multirate Models

## Slide 43: Multirate Model Events
Allows setting model BeginIOStep or EndIOStep functions to execute at an arbitrary rate (for any models)
  The multirate IOStep functions are called at exactly the specified rate, not the normal system IO step rate.
  Normally done in C++ code but API supports registering multirate models via Python
  All models can be used as multi-rate models
  Can choose whether a model should be used in a multi-rate manner or not
  By default model’s rate is in sync with simulation steps
  The IOStep methods are specifically for IO or multi-rate actions. The Hop and integration methods are for state propagation
t
x
x
x
x

## Slide 44: Multirate Model Events
Python API
  For fixed rate:
  Provide a callback function that will determine the next time to execute:
Any model can be used as a fixed-rate or as a multi-rate model
sim.registerMultiRateModel(mdl, <fixed_rate>)
t
x
x
x
x
sim.registerMultiRateModel(mdl, <multirate_callback_fn>)

## Slide 45: Objects as Model Parameters

## Slide 46: Accessing Objects within Models
C++ models often need access to external objects: Terrains, Frames, Nodes, Bodies
Example:
  To set up spring between two bodies, attach the model to node1 one body (Body1)
  How do you get the position of the other end of the sprint on the other body?
    Model encapsulation prevents direct access to the rest of the multibody!
  How can we pass the attach point (node2) on the other body to the model?
There is now a simplified way to get such objects into models as parameters
  In the past we passed in addresses or UUIDs as parameters and cast them (awkward, error-prone)
Body1 with model
Body2
node1
node2

## Slide 47: Improved Object Access within Models
Goals
Provide a unified, consistent way to pass objects into models
The model autocoder should handle the bulk of the work
Simplify C++ model code dealing with objects
Make adding any new object type to be very simple and not require additional non-auto-generated C++ code to handle retrieval and type conversions.

## Slide 48: Model Object Parameters
The model autocoder now supports for ‘object’ parameter types in the model .mdl files to handle objects:
The model autocoder generates code using the ‘Class’ name to cast the objects appropriately. It includes the proper header includes as specified.
Objects are available in model C++ code via params()->xnode (with correct type automatically)
Objects would be passed in when models are created or bound.
[params]
...
[[xframe]]
Type = object
Class = Dframe::Frame*
Header = "DFrame/Frame.h"
Length = -
Description = """Node… """

## Slide 49: Notebook: Passing Objects as Parameters
This notebook shows how to pass objects as parameters to models
  E-Dshell/Part-2-Models/12-Object-Parameters

## Slide 50: Variable Size Model Data

## Slide 51: Variable-size Model Data
We sometimes need to model systems that have variable size data
Example: NlinkSpringDamper
  Model supports N bridles going from confluence point down to N attach points on the body
  Model allows N bridles with separate lengths, spring/damper parameters for each bridle
  We need the ability to set independent parameter data for N bridles!
confluence point
three bridless

## Slide 52: Variable-size model data
Dshell models support variable sized data
  Parameters, scratch, state, flowIns*, flowOuts*, contState
Basics:
  The length of variable-length parameters, scratch, states, and continuous state data can be changed at runtime using this API <mdl>.variableArraySize(‘param.var’, 23)
  Values can be assigned to variable-length data if the length of the incoming data matches the variable existing length – otherwise the length of the variable must be updated first.
  The length of variable-length flowIns/flowOuts is set by the length of the signal they are tied to.
  Variable-length arrays of strings and ‘structs’ are now supported

## Slide 53: Variable-size model data
API (both C++ and Python)
GENERAL:
<mdl>.variableArraySize(“<type>.<var-name>”, <new-value>)
where: <type> is ‘param’, ‘scratch’, ‘state’, or ‘contState’
SPECIFIC:
<mdl>.isParamVariableArraySize(“<param-name>”)  bool
<mdl>.paramVariableArraySize(“<param-name>”, <new-value>)
<mdl>.stateVariableArraySize(“<param-name>”, <new-value>)

## Slide 54: Variable-size model data
Approach
  If the data length needs to be changed at runtime, the length must be updated first.
  The lengths can be set in the model C++ code if the appropriate length can be determined there
  If the model is created and managed by an Assembly (next topic):
    In the assembly that creates the model, add code to the assembly bindParams() function that sets the desired length before assigning values.

## Slide 55: Notebook: Variable Size Data
This notebook shows handling variable size parameter data
  E-Dshell/Part-2-Models/13-Variable-Size-Data

## Slide 56: Activating/Deactivating Models

## Slide 57: Active/Inactive Models
You may want to use different models for the same device/subsystem during a simulation
  Model behavior may change depending on the situation
    Eg, in ground vehicle simulations some terrain-tire models handle different situations better (more details in the ROAMS session)
      Hard soil  Fiala model
      Soft soil  Bekker model
  Although it is possible to have a model which is multi-modal, it is better practice to have single-mode models (simpler to test, maintain, develop, etc)
We can have BOTH models in the same simulation hooked up to the same signals, and switch between them by activating one and deactivating the other

## Slide 58: Active/Inactive Models
Models can be active or inactive
  Models are “active” by default
  A model can be deactivated or activated:
  <mdl>.active(False)
  <mdl>.active(True)
  Model code for inactive models is skipped when during simulation execution
  Model flowOuts are frozen for inactive models

## Slide 59: Notebook: Activating / Deactivating Models
This notebook shows how to activate and deactivate a model at runtime
  E-Dshell/Part-2-Models/11-Active-and-inactive-models

## Slide 60: Dshell Simulation Architecture Implications

## Slide 61: Reuse across Multiple Configurations
Multiple vehicle/simulation configurations
  Testbed and analysis needs often require different variants of the vehicle and the simulation model
Often this need can be met via different choices of the ‘config’ values passed to assemblies
In addition, broader variants can be supported by adding/removing assemblies to a baseline configuration
This can all be done within the context of a simulation design, so we seldom need to create and maintain multiple simulators

## Slide 62: Model Reuse across Projects
Simulations are created based on parameterized component assemblies and models
User scripts define the specific assemblies to be used for a simulation
While user scripts may not be reusable, most of the code they use is kept separate
Thus it is easy to identify, locate and reuse complex component assemblies and models for use in other projects (eg. sensors, vehicle suspensions, aerodynamics, terramechanics etc)
Indeed, many of these components can even be reused across multiple domains (flight dynamics to ground vehicles to robotics)

## Slide 63: Managing Complexity/Brittleness
Vehicle dynamics simulations are notoriously complex and fragile
  Physics is complex
  Models across multiple domains need to interact with each other and the dynamics
Dshell’s object-oriented, component based approach provides an approach for reducing coupling and complexity
Information hiding and encapsulation is critical to this
  Models know nothing about the rest of the simulation other than the node/body/hinge they need
  Such direct access to dynamics objects eliminates the needs for complex and brittle bookkeeping needed with black box dynamics
  Assemblies know nothing about other assemblies in the simulation – or the specifics of their implementation
The limited coupling allows parts of the simulation to change without impacting the rest
  Allows multiple configurations
  Allows easier evolution of the different models within a simulation

## Slide 64: Key Role of DARTS
We have barely mentioned DARTS in the Dshell description – but it is critical to making Dshell work
Critical DARTS features
  Instead of being a typical monolithic dynamics module, DARTS exposes an API and family of objects at all levels – bodies, nodes, hinges, subhinges, subgraphs etc and a rich API
  This makes it possible to hand off nodes and hinges to Dshell models to provide the essential but narrow interface between the models and DARTS
  The DARTS algorithms are structure dependent, i.e. they only care about the current body topology
  This allows us to build up the multibody model incrementally as individual assemblies are added (this can stop at any time)
  Moreover, run-time changes to the topology are not a problem
The Dshell component based approach builds upon the DARTS’ API

## Slide 65: BACKUP

## Slide 66: Recap
What is the purpose of a Dshell model?
  To model components of the system and form an inter-connected dataflow for the system level simulation model
What are examples of Dshell models?
  Actuators, IMUs, encoders, etc
What is inside a Dshell model?
  It has discrete & continuous states, inputs/outputs, parameters
How do the Dshell models interact with the multibody model?
  Through handles to nodes and hinges within the multibody model
What types of Dshell models are there?
  Continuous, Actuator, Sensor, Motor, Encoder, Flow
How do we inter-connect Dshell models into a dataflow?
  Via signals that provide shared data buffers for data space.
How is the calling order of models in the dataflow determined?
  Automatically via the inter-connection.
How do we instance a Dshell model?
  Use Assemblies to create, configure, and connect models
How can we inspect the contents of a Dshell model?
  Dshell Gui, specNodes

## Slide 67: What we did not cover …
Variable size parameters
Re-tying model flowIns/flowOuts
Runtime Debugging
Models are active or NOT
  “active” by default
  A model can be deactivated: m.active(False)
  Model code is skipped when models are normally executed
  Model flowOuts are frozen

## Slide 68: Model Instancing (Notebook: Day2-TuAm-2Models/1-InstanceModel)
Creating signals
Creating models
Setting parameters
Access model specNode
Access signals

## Slide 69: Model Instancing & Inspection (Notebook: Day2-TuAm-2Models/1-InstanceModel, continued)
Continue with previous notebook
Access model specNode
Access signals
Dshell Gui

## Slide 70: Dshell Model Basics
Simulate functionality of vehicle device, component, environment, etc
Self-contained C++ Dshell model for run-time speed
Inter-coupling interfaces limited to just “signal” connections
Aeroforce actuator model
Wind Model
Atm Model
Aero CM model
CM Aero Node
B
aero/sc body
Node
Type of interaction | Where | Model Type
Body pos / attitude, velocity | Node | Sensor
Hinge coordinates, rates | Hinge | Encoder
Apply force/torque to body | Node | Actuator
Apply force/torque to hinge | Hinge | Motor
None | N/A | Flow

## Slide 71: Questions to Address
What is the purpose of Dshell models?
What are examples of Dshell models?
What is inside a Dshell model?
How do the Dshell models interact with the multibody model?
What types of Dshell models are there?
How do we inter-connect Dshell models into a dataflow?
How is the calling order of models in the dataflow determined?
How do we create an instance of a Dshell model?
How can we inspect the contents of a Dshell model?

## Slide 72: Model Object Parameters
Passing in objects during model model binding
modelParamSet() functions will be updated to process the object as a NdartsBaseObject pointer and pass it to the model
Can also use model.setModelLinkerParams here to easily set model parameters from an associated parameter class created with model linker.
The model C++ code will need an autogenerated function to cast the NdartsBaseObject pointer to the actual class. The modelParamSet() and related underlying functions, as well as code in addModel(), will use that function to cast values to the correct final types and do error checking.
def bindParams(self):
# Get the object from live # objects or get the object # from param classes, etc.
self.modelParamSet(name, ‘xframe’, frame_object)

## Slide 73: Model Object Parameters
Passing in objects during model construction:
The swig layer passes the object to the C++ layer as an NdartsBaseObject pointer
processParams() or related code retrieves and casts the dartsBaseObject pointer back to the appropriate class in the ‘params’ data structure
Requires all objects be derived from NdartsBaseObject (okay for frames, nodes, etc, but will require updating terrain objects)
<asm>.addModel(name, 'actuator',
{ 'class' : <model class>,
'MODEL_TIES' : {},
'params' : {
...
‘xframe' : <frame pointer>
}
})