## Slide 1: Dshell Architecture Overview
Abhinandan Jain, Aaron Gaut, Carl Leake, Vivian Steyert, Tristan Hasseler, Asher Elmland, Juan Garcia Bonilla

## Slide 2: DARTS Lab Simulation World
Dynamics
Rigid/flex bodies
Articulation
Attach/detach etc
Devices
Thrusters, IMU,
Cameras etc
Environment
Terrain, Gravity
Atmosphere,
Ephemerides etc
Geometry
CAD parts
Primitives
Visualization
3D graphics
stripcharts
Analysis
Data logging
Parametric
Monte Carlo
Closed-Loop
Flight s/w
Autonomy/Control
Usability
Introspection
CLI, GUIs, Scripting
Docs, Training
Knowledge base
S/W Mgmt
Version control
Build system
Test suite
Reusability
Architecture
Configurability
Refactoring
Deployment
Bundling
Porting
Issue tracking
Evolution
R&D, new applications
new tools & capabilities
Sim Manager
propagation, fsm,
events
Model and Services
Architecture

## Slide 3: Goal: Build a vehicle simulator
Dynamics is only a part of the overall simulator
Also need to model actuator/sensor devices and environment interactions
These other models are tightly coupled with the dynamics module
Control
Software
Actuators
Sensors
Multibody
How we manage the interfaces between the dynamics and device models has a crucial impact on sim brittleness and scalability.

## Slide 4: Simulation Scaling Challenge
Project | Frames | Dvars | Bodies | Models | Signals | Assemblies
Quadcopter | 33 | 2480 | 5 | 20 | 62 | 21
Mars Heli | 112 | 13000 | 22 | 32 | 76 | 21
Rocky8 | 157 | 21750 | 23 | 96 | 294 | 94
HMMWV | 265 | 24115 | 36 | 34 | 92 | 34
Athlete | 250 | 34649 | 43 | 176 | 586 | 182
RoboSimian | 301 | 71310 | 69 | 167 | 341 | 249
Dual-Arm | 508 | 11858 | 41 | - | - | -
ARTEMIS I |  |  |  |  |  | 

## Slide 5: Context
We have seen some of the key pieces, eg. DARTS needed for the modeling physics of complex vehicle dynamics
Even with these in hand, additional challenges remain for building and using heavy-hitting real-life engineering simulations
  Need non-brittle, evolvable/pliable design
  Support for multiple vehicle/testbed configurations
  Reusable across testbeds, projects and domains
  Auditable/traceable implementation for reviews and V&V
  Usable by non-developers

## Slide 6: Dshell Framework

## Slide 7: DARTS/Dshell Architecture Goals
Support modeling a wide range of systems in a variety of domains
  Library of reusable subsystem models
    Single device models (eg, encoder)
    Multi-part subsystem models (set of thrusters)
  Simple to assemble available subsystem models into a full system model
  Straight-forward to adapt/create new domain-specific subsystem models
Manage simulation complexity

## Slide 8: Vehicle Simulation Examples
Rovers
Spacecraft
Aerial

## Slide 9: Notebook: Quadcopter Simulation
E-Dshell/01_Intro_Quadcopter

## Slide 10: Simulations
Simulations CONTAIN:
Vehicle model(s)
  Multibody system, frames, graphics
  Device models, data flows
  “Black board” for data access (DVar)
Sequencing/state machine (FSM)
Event manager
Integrator
Simulations DO:
Time stepping (integration)
Handles events, FSM, logging
Introspection support (DVars, gui)
Event
Manager
Multibody
System
Models & Data Flows
Sequencing
State-Machine
Sub-system
assemblies

## Slide 11: Dshell Models and Dataflow

## Slide 12: Typical Spacecraft Simulation
Multibody has the kinematic, dynamic state of all bodies in simulation
  Large articulations
  Many degrees of freedom
  Rigid & flexible bodies
Component models of devices which interact with the Multibody or model other processes
  Multibody interfaces with sensor/actuator component models to apply forces/torques, extract positions, velocities, etc.
Closing the loop with software
Integrator/time propagator
Control
Software
Component Models
Actuators
Sensors
DARTS
Overall System Model
Hardware bodies

## Slide 13: Key Existing Dshell Models
Wide range of reusable Dshell component models
  Many application areas
    spacecraft, rovers, ground vehicles, robotics, EDL, aircraft, etc
  Range of computational complexity
    Simple (encoders)
    Computationally complex (cameras, terra-mechanics, aero dynamics)
  Variations for different fidelity (eg. thrusters, gravity)
  Class hierarchies
Users can start using the existing models and assemblies right away
Create custom models to match specialized hardware
More info about existing models, etc, in next session

## Slide 14: Quadcopter Models & Data Flows
Vehicle dynamics, devices, environment and controller in closed loop
Fuselage
Rotor 1
Rotor 2
Rotor 4
Rotor 3
Flight
Controller
State
sensor
Thrust, Encoder,
Controller
Thrust, Encoder,
Controller
Thrust, Encoder,
Controller
Thrust, Encoder,
Controller
Gravity
model
fuselage
state
desired rotor speed
rotor speed and torque
cmd
Multibody
model

## Slide 15: Parallels with Simulink
Similar components based approach
  Both use dataflows
  Darts/Dshell predates Simulink
Key difference is the presence of the multibody dynamics block
  Computationally complex
  Has interfaces to most of the models (many signal lines in and out)
  Interfaces depends on the specific mechanism and other models in the sim
  Treat it as a foundational model available to all the other components
  Not built into Matlab/Simulink
Image by By Thomas Haslwanter [CC BY-SA 3.0], via Wikimedia Commons

## Slide 16: Dshell Assemblies (subsystems)

## Slide 17: Recurring subsystems in spacecraft
Similar Thruster Subsystems:
Similar functions/topology
Differing parameters
Generic Thruster Subsystem
Goal:
Create reusable “assemblies” to model generic subsystems
Fuel Lines +
pump + valving
Spacecraft chassis body
Fuel Tank
Thruster

## Slide 18: Recurring subsystems in robotic ground vehicles
Similar Wheel Subsystems:
Similar function/topology
Differing parameters
Generic Wheel Subsystem
Goal:
Create reusable “assemblies” to model generic subsystems
Steer motor + encoder
Wheel drive motor + encoder
Parent body
“Ankle” Body
Wheel

## Slide 19: How to Assemble a Simulation Model
The full simulation model involves many components that need to be created and assembled correctly in order to faithfully model the system
We need a way to assemble the simulation efficiently, take advantage of reusable components/subsystems, and avoid complications of creating everything from scratch each time
We have “templates” for building subsystems, called “Assemblies”
 We need “Assemblies!”
Follow Recipe
Live System Model
System Description

## Slide 20: What is an “Assembly”?
An Assembly is a template for creating a set of signals, models, and sub-assemblies to implement a subsystem
  Each Assembly class is usually a Python class that constructs the desired subsystem using data to customize it
    Topology (eg, number of components)  “config”
    How it relates to the rest of the simulation  “context”
    Parameterization  “params”
  Based on an underlying C++ class for basics
    such as tracking signals created by the assembly
  Primary use in construction phase to construct the multibody, models, and dataflow
    Runtime is all in C++ for speed (unless python functions are used at runtime, eg for events)
  More details about Assemblies in a later session
Multibody
System
Models & Data Flows

## Slide 21: Approaches to Building Simulations
“Pre-fab” approach (baked-in)
  Use an Assembly that creates all of its application-specific children
  Assemblies usually do this for their children
Assembly builder approach (data driven)
  Provide a ‘config’ dictionary to the AssemblyBuilder to create all specified assemblies, etc
Hybrid (typical approach)
  Use combination of above approaches
    Run scripts often use Pre-fab assemblies as sub-assemblies for the “AssemblyBuilder”
Python script
dictionary with describing assemblies to create
AssemblyBuilder digests dictionary and creates the sim
Python script
Instance pre-written Assembly to create the sim

## Slide 22: Relationship between assemblies, Dshell models & multibody
Emergent multibody model
Assembly hierarchy
Asm1
Asm2
Asm3
Asm4
Asm5
mdl1
mdl2
mdl3
mdl4
mdl5
bd1
bd2
bd3
Emergent model dataflow
Run-time
Construction
Factory creating dataflow and multibody models

## Slide 23: Running Simulations

## Slide 24: Simulation Manager – Building Sim
Create simulation executive (manager)
Select/prepare integrator
Create assemblies (which will create models, bodies, etc)
  Apply parameters for multibody, models, assemblies
Set up graphics
Set initial states
Set up simulation runtime logic (events, FSMs)
Set up logging
Execute simulation (step time)
Python
C++
SimulationExecutiveNdarts
Simulation
integrators, multibody, frames, DVar containers, time keeper, scheduler, creates masking I/F, dgui, etc
SimulationExecutiveRoams

## Slide 25: Ways to run a simulation
EDL, Spacecraft
  Run user-created scripts
  Highly customizable
Roams, Helicat
  Dedicated application-specific software, specialized simulation manager, GUI
  No run script
  Limited options for different configurations

## Slide 26: Notebook: Quadcopter Simulation E-Dshell/Part-1-Architecture/01-Intro-Quadcopter
Point out bodies graph, models, and dataflows
Vehicle dynamics, devices, environment and controller in closed loop
Fuselage
Rotor 1
Rotor 2
Rotor 4
Rotor 3
Flight
Controller
State
sensor
Thrust, Encoder,
Controller
Thrust, Encoder,
Controller
Thrust, Encoder,
Controller
Thrust, Encoder,
Controller
Gravity
model
fuselage
state
desired rotor speed
rotor speed and torque
cmd
Multibody
model

## Slide 27: Integration and time stepping
Features of time advancement
Wide number of available integrators
  Fixed, variable step, stiff, non-stiff
Dynamics solvers
  Implicit, explicit, DAE, etc
Multiple rate models
Event handling
Zero-crossing events
  Ability to revert integration steps, eg, for zero-crossing event detection
Done by C++ layer for speed
More details later

## Slide 28: Architectural Advantages

## Slide 29: Controlling Simulation Sequencing Logic
Often need to change simulation behavior as system evolves through different modes over time (eg. EDL sequence)
Finite State Machines offer ability to configure a state/sequencing machine with states and transitions to handle a wide range of simulation events
  Deploying parachutes at set dynamic pressure
  Timed separations
  More details later

## Slide 30: Units Support
Units are supported at the C++ level
  Systems of units (SI, etc)
  Parameters, variables, etc, configured with quantity type (eg, length, time, etc)
  Units derived from system of units and quantity types
  Arbitrary conversions between variables with compatible types supported.
Support for input with unit conversions at python level as well
  Unit conversions consistent between C++ & Python I/O

## Slide 31: Events
Support arbitrary events
  Timed events
  Events that occur at every time step
  Events that occur exactly when a specific condition occurs (zero-crossing)
More details later!
Event
Manager

## Slide 32: Linearization in Dshell
DARTS/Dshell provides tools for full nonlinear system simulation
Linear state space models for control design can be obtained in Dshell
DVar spec nodes
Control
Software
Actuators
Sensors
DARTS
Flexible
Multibody

## Slide 33: Options for Closing the Loop
Need to close the loop with the flight/control software. Options include
  Insert flight software into a model to control other parts of the simulation
  DARTS/Dshell simulation model as stand-in for real system when developing flight software
    MATLAB, Mathematica, other simulation systems
  Replace Dshell Models with actual hardware/software models (Dshell model does I/O with actual device/sw)
I/O with external simulation/model by
  Direct C++ calls
  Socket communication, ROS interface etc
DARTS/Dshell simulation model
External simulation
(manages time)
Control inputs, time step
New state
DARTS/Dshell simulation
Actual Device
Stubbed Device Model
Hardware in the loop
As a subsystem

## Slide 34: Extensive Introspection
Most objects, from vectors, matrices to bodies, models, assemblies etc. have the dump(prefix=‘’) method
  Will generate output with internal info about the object
  The prefix will be applied to each line
  Very useful for debugging and interacting with the sim
New ‘*asDataFrame()’ methods for convenient tabulations of data

## Slide 35: Extensive Error checking
Lots of “assert”-like built in error checking to catch user and other errors. For example
  Catch building of bad SOAQuaternion (non-unity norm)
  Catch creation of bad spatial inertia (inertia not positive semi-definite)
  Catch passing in of bad data (incompatible data or bad types) to assemblies, models etc
  Units checking
  Checks that simulation is in “locked” state before using
These provide a safety net in catching user errors at early stages within a simulation.

## Slide 36: Support for Structural Changes
Need to support structural changes to model during simulation run (eg. body separation, deployment events, touchdown)
Dshell classes have the lockObject() method to put the simulation into a valid state when there are structural changes.
lockObject finalizes an object so that it can be fully used.
  Especially important since many types of configuration changes (add/delete bodies) are allowed at run-time
For example
  Verify that inertia properties are valid for bodies
  Compute the number for DOFs in the multibody system
  Verify that the integrator and its state have been properly set up by the sim
  Verify that a subgraph bodies form a tree
  Resort the order of the models in the data flow
Normal sequence:
  create object, do stuff to it, lock it, use it
  modify object, lock it, use it
Sim.lockObject recursively locks all the objects in the simulation

## Slide 37: Consistent Common Base Class
Most of the C++ simulation classes - frames, bodies, nodes, models, signals, assemblies are derived from a common base class, NdartsBaseObject, hence they all have
  name (not necessarily unique)
  uuid (unique)
  DVar spec node
  lock() method
  can be looked up via their uuid
  dump() method
Helps establish common conventions and usage patterns
NdartsBaseObject
DVar
classes
Frame
Node
Body
Simulation
Model
Hinge
Etc
Signal

## Slide 38: Backup

## Slide 39: Recap
What are the key goals of the DARTS/Dshell architecture?
  Modularity for evolution, reusable components, flexible usage, performance
What are the key elements of a simulation?
  Vehicle model, terrain, environment, 3D, gui, parameters, events/sequencing, integrator
What are the key elements of a vehicle model?
  Multibody model, actuator/sensor/flow models dataflow, control s/w, part geometries, assemblies
How are the elements of a simulation assembled?
  Assemblies create bodies, Dshell models, etc, and put all the parts together to make a complete simulation
How do you run a simulation?
  Use a simulation manager to advance time, simulation
Multibody Dynamics
DARTS
Event
Manager
Multibody
System
Model Data Flow
Sequencing
State-Machine
Dspace
Terrain
Geometry
SimScape
3D Graphics,
GPU Shaders
Data logging
GUIs,
stripcharts
Vehicle/Terrain Interaction
Ephemerides
Sub-system
assemblies

## Slide 40: What is next?
Model basics / details
Assembly basics / details

## Slide 41: Linearization in DARTS
DARTS/Dshell provides tools for full nonlinear system simulation
Linear state space models can be obtained in Dshell
DVar spec nodes
Control
Software
Actuators
Sensors
DARTS
Flexible
Multibody

## Slide 42: Questions to Address
What are the key goals of the DARTS/Dshell architecture?
What are the key elements of the DARTS/Dshell simulations?
What are the key elements of a vehicle model?
How are the elements of a simulation assembled?
How do you run a simulation?

## Slide 43: Start with Basic Quadcopter sim
Basic Quadcopter simulation
Fuselage & 4 rotors
Simplified rotor thrust model
Closed loop flight control
  Eventual goal is to build a flight like simulation

## Slide 44: Quadrotor multibody-centric model (Notebook: 1E-Multibody/3-quadrotor-mechanism)
Create Ndarts model via model file
Add external actuator and gnc blocks
Close the loop with the multibody model

## Slide 45: Quadcopter assembly notebook (Notebook: 1E-Multibody/5-quadrotor-subsystem)
The same quadrotor model, but more compact and extendable using assemblies

## Slide 46: Quadcopter with legs notebook (Notebook: 1E-Multibody/6-quadrotor-legs)
Extending the rotorcraft to add landing legs and terrain contact models