## Slide 1: Units and Quantities 2023 DARTS Lab Course
Abhinandan Jain, Aaron Gaut, Carl Leake, Vivian Steyert, Tristan Hasseler, Asher Elmland, Juan Garcia Bonilla

## Slide 2: Questions To Address
Why worry abut units?
What are “Quantities”
What support does the DARTS/Dshell framework provide for input/output of data in different units systems?
  In C++?
  In Python?

## Slide 3: Typical Scenario
Your simulation Assumes SI Units: meters
You get data in various units
How can you make sure the data gets into your simulation with the correct units using proper conversion constants?
Simulation
Assumes SI units (meters, kg, seconds…)
Data In SI units: meters
OK!
Data In metric units: kilometers
OK?
Data Imperial units: feet
???

## Slide 4: Goals
Purpose of Units Handling
Tag simulation data with quantity type (e.g., length, mass) and catch errors from mismatches
Make simulation models aware of units (eg. meters, feet)
Support user specified unit conversion constants uniformly across C++ and Python
Support different systems of units (SI, US, molecular dynamics)
Enforce units system consistency at C++ level

## Slide 5: Terminology
“Quantity”, “quantity” or “Base Quantity Type”
  The underlying type of quantity (both fundamental quantities and derived quantities)
    Time, Mass, Length, Velocity, Pressure, etc.
‘quantities.py’
  The python quantities.py package and the units definitions it provides (as updated in units.py).
  System of Units
  Select at simulation startup, immutable during run
  Eg: SI/MKS, US, Gneimo

## Slide 6: Notebook to demo units, constants, etc.
Notebook:
  E-Dshell/Part-4C-UnitsQuantities/01-Units-basics

## Slide 7: Under the Hood!

## Slide 8: Approach
C++
Python
Dvar
specs
All data in single units system
(raw numbers, no unit conversions needed or made)
Data may be tagged as units aware quantinties.py data objects
DVar items have quantity type that determines the native units. Support for I/O unit conversions
Unit conversions occur when there is a mismatch between the units of the quantities.py element and the spec

## Slide 9: Consistent Unit Conversions Between C++ and Python

## Slide 10: Conversion Constants
Provides consistent conversion constants to be used in C++ and in the Python ‘quantities.py’ package to ensure end-to-end unit conversion consistency
  C++ header file with conversion constants in DshellEnv
  SWIG-wrapped C++ header file so the conversion constants can be used in Python
  DshellEnv/units/units.py uses the C++ conversion constants (where needed) to override conversion constants in quantities.py to bring it in alignment with the constants in the C++ conversion constants header file.

## Slide 11: Excerpt from unit_conversions.h
Available in C++ as a normal C++ include file
Available in Python using UnitConversions_Py
Conversion constants update with JSC data
namespace Dshell::DUnits
{
// Mass
const double KG_PER_SLUG = 14.59390293720636;
const double KG_PER_LBM = 0.45359237;
…
}

## Slide 12: Excerpts from units.py
Only update values that were different in ‘quantities.py’ from the desired NIST/etc values:
  slug (slugs), lb (lbm, pound, avoirdupois_pound)
  lbf (force_pound, pound_force)
  psi (pound_force_per_square_inch), psf
from quantities import *
from Dshell.UnitConversions_Py import KG_PER_LBM, KG_PER_SLUG
slug._definition = KG_PER_SLUG * kg
slug._conv_ref = slug._definition._reference
lb._definition = KG_PER_LBM * kg
lb._conv_ref = lb._definition._reference
…

## Slide 13: C++ Support for Units

## Slide 14: C++ Support of Units Systems
Allow selection of system of units during simulation initialization
  Default: SI (MKS)
    We provide a SimulationExecutive* startup argument to override units system
  All internal C++ calculations (eg, Dshell/Darts) are in raw form and assume these units.
    No unit conversions happen during these operations
  System of units cannot be changed on the fly

## Slide 15: C++ Units Support
Assign Quantity type info to all DVar specs and signals
Set DVar values using quantity.py data after applying correct unit conversions.
Log variables in user-desired units
Ensure that user interfaces to sim data is in the user desired units

## Slide 16: C++ Support of Units Approach
C++ units header file that defines an enum for basic quantity types (eg, Time, Mass, Length, Velocity, etc) – but not tied to any system of units.
All Dshell / Darts variables will be in raw form and assumed to be in the selected units system
  During internal C++ calculations, no conversions are thus necessary
  During spec node input/output, necessary conversions can be done since we know the variable type and the selected units system. (Use Python 'quantities.py' to do necessary input conversions.)

## Slide 17: Units Implementation Approach
In configuration files:
  Define desired base quantity types
  Construct derived types
Autogenerate the ‘quantities.h’ and ‘units.h’ C++ header file containing enums and other class definitions (occasionally, only as needed)
  Allows robust updating in the future
  Currently/R9: 9 fundamental and 78 derived quantity types
Support for full units handling code in C++
  Base Quantity types
  Units types (for conversions)

## Slide 18: Inputs
Quantity = Time
Quantity = Mass
Quantity = Length
Quantity = Angle
Quantity = SolidAngle
Quantity = Current
Quantity = Temperature
Quantity = Quantity
Quantity = LuminousIntensity
DerivedQuantity = Dimensionless = 1
DerivedQuantity = Avogadro = 1/Quantity
DerivedQuantity = Area = Length^2
DerivedQuantity = Volume = Length^3
DerivedQuantity = FlowRate = Length^3/Time
DerivedQuantity = Density = Mass/Volume
DerivedQuantity = Velocity = Length/Time
DerivedQuantity = AngularVelocity = Angle/Time
DerivedQuantity = Acceleration = Length/Time^2
…
Constant[SI] = const Mass kg = 1;
Constant[SI] = const Length m = 1;
Constant[SI] = const Time s = 1;
Constant[SI] = const Frequency Hz = 1/s;
Constant[SI] = const Current A = 1;
Constant[SI] = const Temperature K = 1;
Constant[SI] = const Quantity mol = 1;
…
For SI…
Will generate separate files/namespaces for each units system

## Slide 19: Excerpt from Generated Header
typedef enum {
// Fundamental quantities
TIME = 1,
MASS = 2,
LENGTH = 3,
ANGLE = 4,
SOLID_ANGLE = 5,
CURRENT = 6,
TEMPERATURE = 7,
QUANTITY = 8,
LUMINOUS_INTENSITY = 9,
// Derived quantities
DIMENSIONLESS = 100, // 1
AVOGADRO = 101, // 1/Quantity
...
POLYHEDRON_LAPLACIAN = 182, // Dimensionless
} BASIC_QUANTITY_ID;

## Slide 20: Unit Systems
Full support for multiple units system (in header files, etc).
  Mostly complete for SI
  Very limited subset for US/Imperial units
Implemented C++, SWIG-wrapped C++, and limited straight Python functionality to look up conversion constants in C++ from Base Quantity Type (for a “To” receiving DVar), in the current system of units, and a “From” object such as a quantities.py input object (for Parameters or other objects)

## Slide 21: Model Quantity Info
Model data items in model definition files (.mdl) need Quantity info
  For each variable that is a double (scalar or vector)
    Include: Quantity = Length # (or appropriate quantity) DerivQuantity = Velocity # (for continuous states)
    Old ‘Units = ‘ lines should be removed
Find quantity names:
  DshellEnv/units/quantities.h
  https://dartslab.jpl.nasa.gov/qa/1240/
Model quantity data is linked automatically when using model linker and param linker.

## Slide 22: Parameters Need Quantity Info
For each float/double data field in your parameter classes, add: quantity=<Quantity> # (eg. Length)
Units should not be baked into Parameter classes
  Generalizes Parameter classes so they can be applied in all unit systems.
Remove units definitions
Data field classes that support quantity:
  FloadDataField, FloatArrayDataField
  FloatOrVector3DataField
  Vector3DataField, Vector3ArrayDataField

## Slide 23: Add Signal Quantity Info
When signals are created (eg, in assemblies), quantity should be specified
  Add extra arguments during signal creation to indicate Quantity: from Dshell.Quantities_Py import FORCE ... self.addSignal('cmdForce', {‘comment’: 'a commanded force', ‘type’: ‘double’, ‘length’: 3, ‘quantity’: FORCE})

## Slide 24: Model Signal Handling
When models are created, they tie signals to flowIns/flowOuts.
  No problem if the quantity types match
  If either side is “Unspecified”, the Quantity type of the other side is copied to it.
    Useful for some models with signals types that are not known in advance, eg, PID models.

## Slide 25: Signal Tie Quantity Handling
Case 1: The quantity of the signal and the model flowIn/flowOut match:
  No problem, connect
Case 2: The quantity of the signal is specified but the quantity of the flowIn/flowOut is not specified:
  Update the flowIn/flowOut to have the same quantity as the connecting signal
Case 3: The quantity of the signal is not known, but the quantity of the flowIn/flowOut is known:
  Update the quantity of the signal to match the flowIn/flowOut
Case 4: The quantity of the signal and flowIn/flowOut are known but do not match:
  ERROR!

## Slide 26: BACKUP