## Slide 1: Quadcopter Reference Problem Part 3 2023 DARTS Lab Course
Abhinandan Jain, Aaron Gaut, Carl Leake, Vivian Steyert, Tristan Hasseler, Asher Elmland, Juan Garcia Bonilla

## Slide 2: Goal: Build a vehicle simulator
Dynamics is only a part of the overall simulator
Also need to model actuator/sensor devices and environment interactions
These other models are tightly coupled with the dynamics module
Control
Software
Actuators
Sensors
Multibody
How we manage the interfaces between the dynamics and device models has a crucial impact on sim brittleness and scalability.

## Slide 3: Quadcopter Models & Data Flows
Vehicle dynamics, devices, environment and controller in closed loop
Fuselage
Rotor 1
Rotor 2
Rotor 4
Rotor 3
Flight
Controller
State
sensor
Thrust, Encoder,
Controller
Thrust, Encoder,
Controller
Thrust, Encoder,
Controller
Thrust, Encoder,
Controller
Gravity
model
fuselage
state
desired rotor speed
rotor speed and torque
cmd
Multibody
model

## Slide 4: Multibody-Centric Design Pattern
Multibody dynamics is complex and involves specialized skills
The dynamics model and solver are traditionally a black box for the simulator
The multibody-centric approach thus builds the central dynamics as a monolithic black box
Device etc models are built separately and integrated with the multibody dynamics
Close the loop with the flight/control software
Control
Software
Actuators
Sensors
Multibody
Artificial divide, in spite of tight coupling, makes the interfaces between the dynamics and device physics complex!

## Slide 5: Problems with this Approach
Adding a rotor, landing leg, camera requires simultaneous changes to the monolithic multibody model, and its complex interfaces to accommodate the new device models
  Easy to get this wrong
  The simulator design is brittle and accommodating changes and extensions is difficult
Design brittleness arises from the monolithic multibody model from the multibody-centric design pattern
5

## Slide 6: Simulation Complexity
Project | Frames | Dvars | Bodies | Models | Signals | Assemblies
Quadcopter | 33 | 2480 | 5 | 20 | 62 | 21
Mars Heli | 112 | 13000 | 22 | 32 | 76 | 21
Rocky8 | 157 | 21750 | 23 | 96 | 294 | 94
HMMWV | 265 | 24115 | 36 | 34 | 92 | 34
Athlete | 250 | 34649 | 43 | 176 | 586 | 182
RoboSimian | 301 | 71310 | 69 | 167 | 341 | 249
Dual-Arm | 508 | 11858 | 41 | - | - | -
ISS Jettison | 64 | 7147 | 4 | 30 | 123 | 28
SLS | 274 | 23230 | 41 | 110 | 614 | 103
PERA | 114 | 6625 | 7 | 46 | 171 | 52
Orion | 251 | 18724 | 32 | 99 | 564 | 118
Mars 2020 | 190 | 32326 | 23 | 60 | 107 | 55
6

## Slide 7: Multibody-Centric Design Pattern
Issues with the multibody-centric design pattern
  Artificial separation between dynamics and device physics models is at odds with the tight coupling between them!
  Treats data and methods as separate entities
  Requires lots of cross coupling and use of global data structures to manage interfaces
  Structural changes in one place have ripple effect of multiple changes in other places
  Difficult to scale up the design
  Complexity growth can box you in!
  Very difficult for anybody but original developers to reuse component models
Dshell uses a different design pattern – that does away with the monolithic multibody model
7

## Slide 8: Subsystem-Centric Design Pattern
Ndarts allows multibody model to be built up incrementally and in a distributed way
The multibody model is an emergent model from building sub-systems
Does away with complex booking and interfaces with device models
DARTS
Control
Software
Actuators
Sensors
At creation, each device model is provided the node/hinge object it needs – so no explicit global interface is needed.

## Slide 9: Use assemblies to create all components of a subsystem
Build up simulations via a hierarchy of assemblies.
Fuselage
Rotor 1
Rotor 2
Rotor 4
Rotor 3
Flight
Controller
State
sensor
Thrust, Encoder
Controller
Thrust, Encoder
Controller
Thrust, Encoder
Controller
Thrust, Encoder
Controller
Gravity
model
Multibody
model
fuselage
state
desired rotor speed
rotor speed and torque
cmd
Rotor assembly

## Slide 10: Single rotor assembly details
A rotor assembly includes a rotor body with a node, coupled to encoder, controller, motor models and thrust model
encoder
controller
motor
thrust
volt
speed
torque
thrust
speed
Rotor body
desired speed
(from flight controller)

## Slide 11: Quadcopter assembly hierarchy
Each rotor assembly creates its body, nodes etc
Assemblies are objects, so can have multiple instances
Rotorcraft
Fuselage
Flight
controller
Gravity
Rotor 1
Rotor 2
Rotor 3
Rotor 4
Motor
Thrust
Motor
Thrust
Motor
Thrust
Motor
Thrust
Assembly containment hierarchy

## Slide 12: Emergent mechanism & dataflow
Emergent multibody model
Assembly hierarchy
Asm1
Asm2
Asm3
Asm4
Asm5
mdl1
mdl2
mdl3
mdl4
mdl5
bd1
bd2
bd3
Emergent model dataflow
Run-time
Construction
Factory creating dataflow and multibody models

## Slide 13: Why sub-system centric design pattern?
The multibody model is not a monolithic module that we explicitly build!
  Built incrementally by the yard
Device models that interact with dynamics have narrow access to the node or hinge they need
  Minimizes coupling and interfaces
  Device models do not know or care about other aspects of the multibody model
Modular and decoupled design
Much easier to modify and scale up
13

## Slide 14
Classes Notebook
(notebook: Quadrotor/06-Classes)
Refactor quadrotor sim using a subsystem centric design
14

## Slide 15: Reusability and tooling
15
A core goal of DARTS/Dshell is reusability of assemblies across a variety of simulations
Want to have tooling that can operate on any assembly
Need a common style and interface to enable reusability and tooling
  Solution: the Dshell Assembly class, which all assemblies are derived from.

## Slide 16: Assembly Notebook (notebook: Quadrotor/07-Assembly)
16
Refactoring the previous notebook to use proper Dshell Assemblies.

## Slide 17: Component Dataflow
17
So far, component modeling has been done using methods of assemblies
Some problems:
Dependencies between components can get complicated, especially if they are across assemblies
Component models may need to be updated at different parts of a simulation step
The model evaluation occurs in Python
Dshell Models are our solution

## Slide 18: Models Notebook (notebook: Quadrotor/08-Model)
18
Refactor the previous assembly notebook to use C++ level Dshell Models instead of Python functions

## Slide 19: Configuration Change Notebook (notebook: Quadrotor/09-Config_change)
19
Now that we are using a subsystem centric design, configuration changes are much easier
Notebook: convert the quadrotor simulation to a coaxial helicopter
Imagine the steps required to do this with a multibody centric design.

## Slide 20: Advanced Simulation Scheduling
20
So far we have been stepping the sim uniformly at a fixed rate
Sometimes there is a need for more advanced scheduling:
  Models that update irregularly or at a rate different from the rest of the sim (multirate models)
  Events that must occur exactly when a condition is met, even if it’s between steps (step validation)

## Slide 21: Advanced Scheduling Notebook (notebook: Quadrotor/10-Multirate)
21
Exercising advanced time stepping functionality:
  Add a sensor model that updates at 1 Hz
  Cut off rotors for landing at a precise altitude