## Slide 1: Computer Graphics for Engineering Models 2023 DARTS Lab Course
Abhinandan Jain, Aaron Gaut, Carl Leake, Vivian Steyert, Tristan Hasseler, Asher Elmland, Juan Garcia Bonilla

## Slide 2: Where does this topic fit in the big picture?
Dynamics
Rigid/flex bodies
Articulation
Attach/detach etc
Devices
Thrusters, IMU,
Cameras etc
Environment
Terrain, Gravity
Atmosphere,
Ephemerides etc
Geometry
CAD parts
Primitives
Visualization
3D graphics
stripcharts
Analysis
Data logging
Parametric
Monte Carlo
Closed-Loop
Flight s/w
Autonomy/Control
Usability
Introspection
CLI, GUIs, Scripting
Docs, Training
Knowledge base
S/W Mgmt
Version control
Build system
Test suite
Reusability
Architecture
Configurability
Refactoring
Deployment
Bundling
Porting
Issue tracking
Evolution
R&D, new applications
new tools & capabilities
Sim Manager
propagation, fsm,
events

## Slide 3: Ground vehicle component assemblies
Scenario
Vehicle1
Vehicle2
Software
Hardware
Chassis
Arm
link 1
link n
Mast
link 1
link n
Wheels
wheel 1
wheel n
Suspension
Left
Right
Sensors
Cameras
Front
Nav
IMU
Environment
SunPosition
SunSensor
Motors
Contact
Locomotion
Navigation
Gravity
…
…
…
…

## Slide 4: Motivation

## Slide 5: Motivation
Provide engineering simulation
  Perception systems
  mobility, obstacle detection, path planning
  landing
  camera/lidar sensor modeling
  Non-ideal configurations (noise, distortion, etc)
  Solar radiation pressure modeling
  Solar panel exposure modeling

## Slide 6: Geometry Processing Needs
Geometry
Meeting simulation needs can involve multiple geometry engines using the geometry model data
3D Graphics
position & orientation updates from sim
visualization, playback, camera/lidar sensor modeling
Computational
geometry
collision detection, landing, mobility, comm. modeling, obstacle detection, path planning
Raytracing
sensor modeling, high-end rendering
etc.

## Slide 7: Geometry Processing Engines
Geometry
There are multiple of geometry engine providers with varying functionality and APIs.
3D Graphics
OpenGL, Ogre3D, Coin3D, OpenInventor, OpenSceneGraph …
Computational
geometry
Bullet, FCL, PQP, ANN …
Raytracing
Blender, Optix, Maya …
etc.
position & orientation updates from sim

## Slide 8: Visualization vs Sensor Modeling
Visualization and camera modeling overlap in significant ways
Need sensors other than mon-RGB cameras
  stereo cameras, lidar, radar, etc
Visualization needs:
  Fast, interactive renderings to a user (with a window)
  Helpful debug information (trails, boxes, text, frustums, etc
Sensor modeling needs
  Specific model implementations (may need to be high fidelity)
  Camera: non-ideal lens models
  Lidar: different lighting and material properties/parameters

## Slide 9: Engineering Simulation and Analysis

## Slide 10: Synthetic Generation of Camera Stereo Pair Images
ROAMS
distance
height
Terrain Model
Camera models
Simulated stereo image pair
Stereo processing
Range & Elevation maps
Uses CAHVORE camera model parameters: different locations of cameras, non-aligned optical axes, off-center optical axes etc., radial distortion in next phase.
Stereo software successfully extracts range map from images.
Enables testing of navigation and stereo in the loop for rover mobility and instrument placement scenarios

## Slide 11: Improving visual fidelity
Projects are starting to want higher fidelity camera renders to feed into perception algorithms.
Figure 1: Standard OpenGL renderer used by our camera models.
Figure 2: High quality Blender renderer. Ray-traced backends like Blender and Optix are capable of higher fidelity than our OpenGL renderer.
Goal: Generalize camera models to work with any renderer

## Slide 12: CAHVORE Camera Modeling
The Dshell++ camera models simulate radial and fish-eye distortion in camera lenses and make use of Dspace's offscreen rendering capability as part of the camera modeling process, to achieve real-time performance when operating with the simulation in a closed-loop mode.

## Slide 13: Lidar simulation

## Slide 14: Engineering Analysis
Dspace’s rendering engine can be used to perform compute intensive operations such as vehicle camera modeling, horizon scan, line of sight computation and solar array power analysis

## Slide 15: OptixScene for sensor modeling with reconfigurable pipeline
Using real-time ray/path tracing DARTS/IRIS engine
IRIS supports perception sensor simulation for in-the-loop autonomy development and testing
  But can also be used for rendering/visualization
IRIS has a configurable sensing pipeline
GPU/CUDA hardware accelerated ray tracing
Full control over
  Ray definitions
  Ray generation and tracing
  Material and lighting functions
Raytracing
Action Graph
Filter
Graph
Actions to set up scene geometry & update materials
Filters perform arbitrary logic on data buffer
Rendering

## Slide 16: OptixScene reconfigurable pipeline: camera example
Raytrace Render
image
Lens Distortion
Hapke Model
Material
Properties
CAHVORE
Parameters
scene
Clipmap Update
Optix Build
Action Graph
(Scene Updates)
DEM
Jitter Accumulate
Vignette
Access Filter
Noise
Filter Graph
(Image Modification)
Noise
Parameters
Output
Sensor
Image
Output
Raytracing
Action Graph
Filter
Graph
builds upon NVIDIA’s Optix CUDA based,
GPU-accelerated backward ray-tracing engine
Configurable Optix pipeline

## Slide 17: Camera Sensor Lens Models
Camera
  Adjustable Lens Model
    Pinhole, Fisheye, Spherical, CAHV(OR(E))
  Jitter/Anti-Aliasing
Lens model implemented via ray distortion on GPU
Pinhole
FishEye
Spherical
CAHV
CAHVOR
CAHVORE

## Slide 18: Supported Camera Effect Filters
Brightness
Gaussian blur + grayscale
Negative
Original
Gaussian noise
Vignette
Contrast

## Slide 19: LIDAR Sensor Models
Models supported:
  Uniform grid of beams specified based on :
    Horizontal/Vertical FOV
    Resolution (Number of Horizontal/Vertical Layers)
  User-defined array of beams:
    each with an arbitrary source and direction in the sensor frame
Shaders supported:
  Diffuse
  Distance
Point cloud colored by distance overlaid on terrain
Lidar attached to descent vehicle
Point cloud overlaid onto camera output

## Slide 20: Solar Radiation Pressure Model
Compute force and moment on spacecraft due to radiation
Ray traced model
  Leverages geometry and the scene
  Uses rays to sample the incident radiation on the spacecraft
  Calculates force from material properties
  Includes shadowing effects
Solar radiation
spacecraft

## Slide 21: Cameras exposed to simulation through Dshell
CamImageSynthAltModel
CameraImage
DspaceOgreOffscreenRenderer
dsOffscreenViewport
DOptixCamera
Dshell
Renderer
OptixCahvoreCameraModel
DOptixCamera
Legacy Model
New Model

## Slide 22: Lidar exposed to simulation through Dshell ​
Instantiate via OptixLidarAssembly
  Configures model, context, parameters
OptixLIDARModel deals with frequency and connections in simulation
  Multirate model
Creates a DOptixLidarSensor to generate point cloud from the scene
OptixLidarAssembly
OptixLIDARModel
DOptixLidarBeamsCustomSensor
Lidar Dshell Model

## Slide 23: SRP exposed to simulation through Dshell
Instantiate via OptixSRPAssembly
  Configures model, context, parameters
SRP is an actuator
  Applies force/moment to body
Creates a DOptixSRPSensor to calculate force and moment from radiation
OptixSRPAssembly
OptixSRPModel (actuator)
DOptixSRPSensor
SRP Dshell Model

## Slide 24: Wrap up
Graphics not just for visualization
Primarily leverage OptixScene
  These problems map well to ray tracing
Supported in Dshell
  Cameras (mono and stereo)
  Lidar (custom configurations)
  SRP (actuator)
Flexible pipeline for modeling new sensors and needs
  e.g. can support time-evolution during ray tracing